## Slide 1: Chapter 4 The von Neumann Model
计算机系统概论
Introduction to Computing Systems
（ CS1002A.02）
计算机科学与技术学院
School of Computer Science and Technology

## Slide 2
Outline
Review
1
3
A Machine Structure：von Neumann Model
2
From ENIAC to the Stored Program Computer
4
Summary

## Slide 3
Outline
Review
1
3
A Machine Structure：von Neumann Model
2
From ENIAC to the Stored Program Computer
4
Summary

## Slide 4: Review
MOS transistors are used as switches to implement logic functions.
  N-type: connect to GND, turn on (with 1) to pull down to 0
  P-type: connect to +2.9V, turn on (with 0) to pull up to 1
Basic gates: NOT, NOR, NAND
  Logic functions are usually expressed with AND, OR, and NOT
Properties of logic gates
  Completeness
    can implement any truth table with AND, OR, NOT
  DeMorgan's Law
    convert AND to OR by inverting inputs and output

## Slide 5: Review
We’ve touched on basic digital logic
  Transistors
  Gates
  Storage (latches, flip-flops, memory)
  State machines
Built some simple circuits
  adder, subtracter, adder/subtracter，Incrementer
  Counter (consisting of register and incrementer)
  Hard-coded traffic sign state machine
  Programmable traffic sign state machine
Up next: a computer as a state machine

## Slide 6: Bottom up approach
Transistor Physical Layout
Scheme for
Representing Information
Register Transfer Level (RTL) Design
1K~10K Cells/Module
(100K Devices)
ALU
Full Adder
Gate Level Design
Circuit Level Design
（Transistor Level Design）
(2~8 Devices/Gate)
Register Transfer Level (RTL) Design
2~16 Gates/Cell
(16~64 Devices)
Clk
Register
+
Cout
S
A
B
Cin
Integrated Circuit Design
100 Modules/ IC
0.25M~20G Devices

## Slide 7: Today
Great Idea #2: Stored program computer(Von Neumann Model--A Machine Structure
  Basic Components for a machine
  The LC-3: An Example of von Neumann Machine
  Instruction Processing

## Slide 8: Bottom up approach
Electronic System Level (ESL)Design
Motherboard Circuit Design
10 ICs/ PCB
1~50G Devices
Personal Computer:
Hardware & Software Design
1~10PCBs/System
Integrated Circuit Design
100 Modules/ IC
0.25M~20G Devices
Now, You are Here.

## Slide 9: Great Idea #3: Abstraction Helps Us Manage Complexity
Solve a system of equations
Gaussian
elimination
Jacobi
iteration
Red-black SOR
Multigrid
FORTRAN
C
C++
Java
Intel x86
Sun SPARC
IBM PowerPC
Pentium 4
Core 2 Duo
AMD Athlon X2
Ripple-carry adder
Carry-lookahead adder
Static CMOS
Dynamic CMOS
Nanomechanical
Algorithm and Data Structure
Gates/Register-Transfer Level (RTL)
Application
Instruction Set Architecture (ISA)
Operating System/Virtual Machines
Microarchitecture
Electronic Devices
Programming Language/Compiler
Analog/Digital Circuits
Physics

## Slide 10: Great Idea #4: Software and Hardware Co-design
Software
Hardware
Application
Language
Machine Architecture, ISA
Microarchitecture
Logic and IC
Device
Algorithm & Data Structure
Computer System: Layers of Abstraction
Now, You are Here.
Notes: 10

## Slide 11
Outline
Review
1
3
A Machine Structure：von Neumann Model
2
From ENIAC to the Stored Program Computer
4
Summary

## Slide 12: The First Electronic Computers

## Slide 13: ENIAC - The first electronic computer ,1946年
Programmed by plugboard and switches, time consuming!

## Slide 14: ENIAC - The first electronic computer ,1946年
Changing the program could take days!

## Slide 15: The Origin of the Stored Program Computer
John von Neumann,
c. 1955 Credit: Computer History Museum
1946: ENIAC
  Presper Eckert and John Mauchly -- first general electronic computer.
  Hard-wired program -- settings of dials and switches.
1944: Beginnings of EDVAC(Electronic Discrete Variable Automatic Computer)
  John von Neumann joined ENIAC team and proposed a stored program computer called EDVAC
1945: John von Neumann
  John von Neumann wrote "First Draft of a Report on the EDVAC" in which he outlined the architecture of a stored-program computer.
The basic structure proposed in the draft became known as the “von Neumann machine” (or model).
a memory, containing instructions and data
a processing unit, for performing arithmetic and logical operations
a control unit, for interpreting instructions

## Slide 16: The Stored Program Computer Architecture (von Neumann Machine Architecture or Model)
Output
Devices
Input
Devices
Memory
Programs & Data
Memory Data Register
Memory Address Register
Central Processing Unit
Temporary
Memory
Registers
A
B
Arithmetic Logic Unit
Control Unit
Instruction Register
Program Counter
Data & Adrress Bus
Control Bus

## Slide 17: The Stored Program Computer
Electronic storage of programming information and data eliminated the need for the more clumsy methods of programming, such as punched paper tape — a concept that has characterized mainstream computer development since 1945.
EDSAC
University of Cambridge
UK, 1949
Maurice Vincent Wilkes

## Slide 18: Two major inventions of the microprocessor chip
Stored program + Transistor technology
Change the program so that you can do all kinds of tasks on the same hardware
The device is smaller and faster than a vacuum tube

## Slide 19
Outline
Review
1
3
A Machine Structure：von Neumann Model
2
From ENIAC to the Stored Program Computer
4
Summary

## Slide 20: von Neumann Model

## Slide 21
SR1
16
SR2
3
SR2MUX
16
16
16
16
[10:0]
16
16
SEXT
SEXT
SEXT
[8:0]
[5:0]
[4:0]
SEXT
MEM.EN,R,W
16
MEMORY
MUX
MUX
MDR
…
+
16
16
16
16
ADDR1MUX
2
PCMUX
+1
16
MARMUX
SEXT
[7:0]
GateMARMUX
LD.PC
16
16
16
ADDR2MUX
16
LD.MDR
MUX
MIO.EN
GateMDR
16
16
16
ALU
A
B
ALUK
2
FINITE STATE MACHINE
N
Z
P
RUN
LD.IR
IR
16
DR
LD.REG
REG FILE
SR1
OUT
SR2
OUT
3
3
16
GateALU
LOGIC
16
LD.CC
PC
MAR
16
LD.MAR
LC-3 Data Path
EA
OP
EX
S
F
D
GatePC
Control Unit
Processing Unit
Memory Unit
INPUT
OUTPUT

## Slide 22: Memory
k x m array of stored bits (k is usually 2n)
Address
  unique (n-bit) identifier of location
Contents
  m-bit value stored in location
Basic Operations:
LOAD
  read a value from a memory location
STORE
  write a value to a memory location
•
•
•
0000
0001
0010
0011
0100
0101
0110
1101
1110
1111
00101101
10100010

## Slide 23: Interface to Memory
How does processing unit get data to/from memory?
MAR: Memory Address Register
MDR: Memory Data Register
To read a location (A):
  Write the address (A) into the MAR.
  Send a “read” signal to the memory.
  Read the data from MDR.
To write a value (X) to a location (A):
  Write the data (X) to the MDR.
  Write the address (A) into the MAR.
  Send a “write” signal to the memory.

## Slide 24: Processing Unit
Functional Units
  ALU = Arithmetic and Logic Unit
  could have many functional units. some of them special-purpose (multiply, square root, …)
  LC-3 performs ADD, AND, NOT
Registers
  Small, temporary storage
  Operands and results of functional units
  LC-3 has eight register (R0, …, R7)
Word Size
  number of bits normally processed by ALU in one instruction
  also width of registers
  LC-3 is 16 bits

## Slide 25: Input and Output
Devices for getting data into and out of computer memory
Each device has its own interface, usually a set of registers like the memory’s MAR and MDR
  LC-3 supports keyboard (input) and console (output)
  keyboard: data register (KBDR) and status register (KBSR)
  console: data register (CRTDR) and status register (CRTSR)
  frame buffer: memory-mapped pixels
Some devices provide both input and output
  disk, network
Program that controls access to a device is usually called a driver.
Notes: 25

## Slide 26: Control Unit
Orchestrates execution of the program
Instruction Register (IR) contains the current instruction.
Program Counter (PC) contains the address of the next instruction to be executed.
Control unit:
  reads an instruction from memory
    the instruction’s address is in the PC
  interprets the instruction, generating signals that tell the other components what to do
    an instruction may take many machine cycles to complete

## Slide 27: Instruction Processing（State Transtion）
Decode instruction
Evaluate address
Fetch operands from memory
Execute operation
Store result
Fetch instruction from memory
EA
OP
EX
S
F
D
Notes: 27

## Slide 28: Instruction
The instruction is the fundamental unit of work.
Specifies two things:
  opcode: operation to be performed
  operands: data/locations to be used for operation
An instruction is encoded as a sequence of bits. (Just like data!)
  Often, but not always, instructions have a fixed length, such as 16 or 32 bits.
  Control unit interprets instruction: generates sequence of control signals to carry out operation.
  Operation is either executed completely, or not at all.
A computer’s instructions and their formats is known as its Instruction Set Architecture (ISA).
  Persistent ISA invented by UW grad Gene Amdahl (IBM 360)

## Slide 29: Example: LC-3 ADD Instruction
LC-3 has 16-bit instructions.
  Each instruction has a four-bit opcode, bits [15:12].
LC-3 has eight registers (R0-R7) for temporary storage.
  Sources and destination of ADD are registers.
“Add the contents of R2 to the contents of R6, and store the result in R6.”

## Slide 30: Example: LC-3 LDR Instruction
Load instruction -- reads data from memory
Base + offset mode:
  add offset to base register -- result is memory address
  load from memory address into destination register
“Add the value 6 to the contents of R3 to form a memory address. Load the contents stored in that address to R2.”

## Slide 31: Instruction Processing: FETCH
Load next instruction (at address stored in PC) from memory into Instruction Register (IR).
  Load contents of PC into MAR.
  Send “read” signal to memory.
  Read contents of MDR, store in IR.
Then increment PC, so that it points to the next instruction in sequence.
  PC becomes PC+1.
EA
OP
EX
S
F
D

## Slide 32: Instruction Processing: DECODE
First identify the opcode.
  In LC-3, this is always the first four bits of instruction.
  A 4-to-16 decoder asserts a control line corresponding to the desired opcode.
Depending on opcode, identify other operands from the remaining bits.
  Example:
    for ADD, last three bits is source operand #2
    for LDR, last six bits is offset
EA
OP
EX
S
F
D

## Slide 33: Instruction Processing: EVALUATE ADDRESS
For instructions that require memory access, compute address used for access.
Examples:
  add offset to base register (as in LDR)
  add offset to PC (or to part of PC)
  add offset to zero
EA
OP
EX
S
F
D

## Slide 34: Instruction Processing: FETCH OPERANDS
Obtain source operands needed to perform operation.
Examples:
  read data from register file (ADD)
  load data from memory (LDR)
EA
OP
EX
S
F
D

## Slide 35: Instruction Processing: EXECUTE
Perform the operation, using the source operands.
Examples:
  send operands to ALU and assert ADD signal
  do nothing (e.g., for loads and stores)
EA
OP
EX
S
F
D

## Slide 36: Instruction Processing: STORE
Write results to destination. (register or memory)
Examples:
  result of ADD is placed in destination register
  result of memory load is placed in destination register
  for store instruction, data is stored to memory
    write address to MAR, data to MDR
    assert WRITE signal to memory
EA
OP
EX
S
F
D

## Slide 37: Changing the Sequence of Instructions
In the FETCH phase, we incremented the Program Counter by 1.
What if we don’t want to always execute the instruction that follows this one?
  examples: loop, if-then-else, function call
Need special instructions that change the contents of the PC.
These are called jumps and branches.
  jumps are unconditional -- they always change the PC
  branches are conditional -- they change the PC only if some condition is true (e.g., the contents of a register is zero)

## Slide 38: Example: LC-3 JMP Instruction
Set the PC to the value contained in a register. This becomes the address of the next instruction to fetch.
“Load the contents of R3 into the PC.”
Notes: 38

## Slide 39: Driving Force: The Clock
The clock is a signal that keeps the control unit moving.
  At each clock “tick,” control unit moves to the next machine cycle -- may be next instruction or next phase of current instruction.
Clock generator circuit:
  Based on crystal oscillator
  Generates regular sequence of “0” and “1” logic levels
  Clock cycle (or machine cycle) -- rising edge to rising edge
“1”
“0”
time
Machine
Cycle

## Slide 40: Control Unit State Diagram
The control unit is a state machine. Here is part of a simplified state diagram for the LC-3:
A more complete state diagram is in Appendix C.
It will be more understandable after Chapter 5.

## Slide 41: Stopping the Clock
Control unit will repeat instruction processing sequence as long as clock is running.
  If not processing instructions from your application, then it is processing instructions from the Operating System (OS).
  The OS is a special program that manages processor and other resources.
To stop the computer:
  AND the clock generator signal with ZERO
  when control unit stops seeing the CLOCK signal, it stops processing

## Slide 42
Outline
Review
1
3
A Machine Structure：von Neumann Model
2
From ENIAC to the Stored Program Computer
4
Summary

## Slide 43: Von Neumann Model

## Slide 44: Instruction Processing Summary
Instructions look just like data -- it’s all interpretation.
Three basic kinds of instructions:
  computational instructions (ADD, AND, …)
  data movement instructions (LD, ST, …)
  control instructions (JMP, BRnz, …)
Six basic phases of instruction processing:
  not all phases are needed by every instruction
  phases may take variable number of machine cycles
EA
OP
EX
S
F
D

## Slide 45: LC-3 Data Path